## Slide 1: Sustainability in HPC: Vision and Opportunities
Mohak Chadha1, Eishi Arima1, Amir Raoofy2,
Michael Gerndt1, Martin Schulz1,2
1 Technische Universität München (TUM)
2 Leibniz-Rechenzentrum (LRZ)

## Slide 2: Executive Summary
We will discuss potential solutions to reduce the carbon footprint of supercomputers from various perspectives (this is a position paper)
  Carbon Emission = Direct (Scope 1) + Indirect (Scope 2/3)
  Scope 2: Operational Carbon
  Scope 3: Embodied Carbon
Carbon Reduction
Scope 2
Scope 3
Component (or Chip) Design
System Design & Procurement
System Lifetime, Reuse, & Recycle
Dynamic Power Bound Scaling
Dynamic Resource Scaling
Scheduling & Checkpointing
Making HPC Users Greener

## Slide 3: Outline
Background
Reducing Embodied Carbon (Scope 3)
Reducing Operational Carbon (Scope 2)
Conclusion & Acknowledgement

## Slide 4: Outline
Background
Reducing Embodied Carbon (Scope 3)
Reducing Operational Carbon (Scope 2)
Conclusion & Acknowledgement

## Slide 5: Needs for Carbon-awareness in Supercomputing
Supercomputers indirectly account for a tremendous amount of carbon emissions
  Mainly due to the scale: (1) consist of over 100K of components; (2) consume few 10s MW of power
Need to limit their carbon emissions while following the GHG (Green House Gas) protocol
Future Green Supercomputers
(Image generated by deep AI)
Frontier
1.2Exa @23MW
Fugaku
0.44Exa @30MW
Aurora
2Exa? @60MW?
Carbon
Awareness

## Slide 6: The GHG Protocol
Scope 1: Relevant if fossil fuels are burnt on site (usually not the case)
Scope 2: Electricity, heating, cooling, etc. for the site operation
Scope 3: The other indirect emissions, e.g., production, shipping, and disposal of system components
Source: https://ghgprotocol.org/sites/default/files/standards/Corporate-Value-Chain-Accounting-Reporing-Standard_041613_2.pdf
Our Focus

## Slide 7: Outline
Background
Reducing Embodied Carbon (Scope 3)
Reducing Operational Carbon (Scope 2)
Conclusion & Acknowledgement

## Slide 8: Reducing Embodied Carbon (Scope 3)
Embodied carbon consists of production, transportation, & disposal
  The production part (manufacturing + packaging) is dominant [U. Gupta+ ISCA’22]
  The embodied carbon trend differs across different systems
    The system architecture & procurement (incl. product choices for components) matter
Estimated Embodied Carbon Footprint Breakdowns
Calculated based on a prior study [B. Li + SC’23]
Promising Approaches for Embodied Carbon Reduction:
  Carbon-aware Component Design
  Carbon-aware System Architecture & Procurement
  System Lifetime Extension & Reuse/Recycling

## Slide 9: Designing Carbon-efficient HPC Components
Conventional Chip Design:
max Perf(W, d)
s.t. Pow(W, d) ≤ PowTarget
Cost(d) ≤ CostTarget
d ∈ D
In: W, Out: dopt (∈ D)
Carbon-aware Chip Design:
max Perf(W, d)
s.t. Pow(W, d) ≤ PowTarget
Cost(d) ≤ CostTarget
EmCrbn(d) ≤ EmCrbnTarget
OpCrbn(W, d, CI) ≤ OpCrbnTarget
d ∈ D
In: W, CI, Out: dopt (∈ D)
W: Target workloads or proxy apps
D: A set of design points to explore
d (∈ D): A set of design parameters
XTarget: Target value for metric X
EmCrbn/OpCrbn: Embodied/operational carbon
CI: Typical carbon intensity of the target system
Hierarchical Optimization for 2.5D/3D Integrations:
Alternative design goals [U. Gupta+ ISCA’22]:
Carbon-delay product
Carbon-delay2 product
Embodied Carbon in Production
≃ Manufacturing + Packaging
Chiplet A for WX
2.5D/3D Packaging
Chiplet A for WX
Chiplet A for WX
Chiplet A for WX
Chiplet A for WX
Chiplet A for WX
Chiplet A for WX
Chiplet B for Wy
Chiplet A for WX
Chiplet A for WX
Chiplet A for WX
Chiplet C for Wz
Both inter- and intra-chiplet optimizations matter!
* inter: manufacturing part, intra: packaging part

## Slide 10: System Architecture and Procurement
Embodied Carbon Constraint
System Optimization
Goal: Max SystemThroughput(Workloads)
Constraints:
Budget = MachineCost + Electricity;
SystemFootprint; SystemWeight;
CoolingCapacity; PowerSupply
New Constraint: CarbonBudget
Total Carbon Budget
Embodied Carbon Budget
+
Operational Carbon Budget
Trade-off
∝ System’s Energy Budget
CPUA
Perf: 2, Pow: 1
Cost: 1, EC: 2
CPUB
Perf: 1.5, Pow: 1
Cost: 1, EC: 1
. . . .
GPUA
. . . .
GPUB
. . . .
MemA
MemB
. . . .
. . . .
The same procedure goes for all the other components
Best in Performance
Best in Embodied Carbon
The optimal system design will change by taking carbon into account!
The decision will be even harder due to the emerging architectures/devices!

## Slide 11: System Lifetime, Reuse, and Recycling
System Lifetime: Typically 4-6 years
  Extending the lifetime will contribute to the embodied carbon reduction (right fig)
Reuse & Recycling: for reducing the carbon emissions in disposal & production
  Reuse: LRZ offers decommissioned machines to other public institutions for free
  Recycling: DRAM chips (DDR4=>DDR5), heat pipes, etc.
HPC System | Start of Operation | Decommissioned
SuperMUC | 2012 | 2018
SuperMUC Phase2 | 2015 | 2019
SuperMUC-NG | 2019 | 2024
SuperMUC-NG Phase2 | 2023 | –
4-6yrs
Embodied
Operational
Year
Carbon/year
Year
Carbon/year
Longer Lifetime

## Slide 12: Outline
Background
Reducing Embodied Carbon (Scope 3)
Reducing Operational Carbon (Scope 2)
Conclusion & Acknowledgement

## Slide 13: Reducing Operational Carbon (Scope 2)
Operational Carbon Footprint =
Carbon intensity depends on the location and can change over time
Promising Approaches: Scaling or shifting the following properties in accordance the carbon intensity
  System Power Bound
  System Scale (# of nodes)
  Peak Load
* Existing energy/power reduction techniques generally ignore the carbon intensity

## Slide 14: Carbon-aware Dynamic Power Budget Scaling
A new use case of HPC PowerStack
Scaling up/down the total system power bound based on the carbon intensity
  Goal: to limit the operational carbon footprint within a given target
Carbon-aware Dynamic Power Budget Scaling Here
https://hpcpowerstack.github.io/
Hierarchical Power Mgmt
Time
Carbon Intensity
or Power Bound
Carbon Intensity
System Power Bound
The Concept
High
High
Low
Low
REGALE PowerStack
+
Carbon Intensity Estimation Tools
https://www.watttime.org/
e.g., watttime
Promissing Solution

## Slide 15: Carbon-aware Dynamic Resource Scaling
Dynamically adapt the system scale in accordance with the carbon intensity
Change the resource assignments to running jobs – known as malleability
  Should cooperate with power budgeting
Time
Carbon Intensity
or Total # of Nodes
Carbon Intensity
Total # of Nodes
The Concept
Grow
Low
Shrink
High
Hierarchical/Dynamic Res. & Pow Mgmt
Low Carbon Intensity
High Carbon Intensity
JobA
JobB
JobC
Off
JobB
JobC
JobA
Node Power Bound: High
Low
Ongoing Efforts toward Malleability Support
Our Projects:
Closs Layer Support:
+
PMIx
+

## Slide 16: Carbon-aware Scheduling and Checkpointing
Concept: Adapt the system loads so as to have less jobs/loads when the carbon intensity is higher
Promising Solution: Peak Load Shifting
  Proactive: predict the duration of green (low carbon intensity) period and optimize the scheduling decisions (e.g., green period-aware backfilling)
  Reactive: suspending, checkpointing, and restarting (large) jobs
Time
Carbon Intensity
or System Load
Carbon Intensity
System Load
Peak
High
Low
×
Peak
Shifting
Time
Carbon Intensity
or System Load
Carbon Intensity
System Load
Peak
High
Low
○

## Slide 17: Making HPC Users Greener
Users can also contribute to peak shifting & energy footprint reduction
  Peak shifting: by submitting their jobs in a green queue
    Economical & low priority if not in the green period
    Accept power capping, scale shrink, or suspend
  Energy footprint reduction: by job-level optimizations for energy reduction
    Code optimizations, energy-efficient libraries, etc.
Should provide right feedback & incentives to users to make them green
OMG
Energy
Efficient
Job
Green Q
–
Carbon-based accounting
System Mngr
Monitor
Examon
System
User
Feedback/Suggestions
Your job accounted for the same amount of CO2 emissions as xxxxx, and as a result it consumed yy% of quota assigned to your project! You could save zz% of the quota consumption by simply following the steps below…
Current HPC: Time is money and money is time
Future HPC: Carbon is money and money is carbon

## Slide 18: Outline
Background
Reducing Embodied Carbon (Scope 3)
Reducing Operational Carbon (Scope 2)
Conclusion & Acknowledgement

## Slide 19: Concluding Remarks
Carbon-aware supercomputing ≠ power-/energy-aware supercomputing!
Embodied Carbon Reduction (Scope 3): Needs an end-to-end carbon-aware optimization from chip to system, and even procurement
Operational Carbon Reduction (Scope 2): Needs (1) adaptive power, resource, & job management, and also (2) green users

## Slide 20: Acknowledgement
This work has received funding under the European Commission’s EuroHPC and Horizon 2020 programmes under grant agreements no. 956560 (REGALE), no. 955606 (DEEP-SEA), and no. 955701 (TIME-X).
CAPS TUM
REGALE
TIME-X
DEEP-SEA
CAPS TUM
LRZ
Booth
Feel free to contact us!
Visit our booth (#1311)!